## Slide 1
SIMATS ENGINEERING
ASSESSMENT TOOL 1
COURSE NAME:
CSA0704 : Computer Networks
COURSE OUTCOME COVERED
CO1: Apply the functions of OSI layer in enabling reliable data transmission across networks. (BL2, BL3)
Assessment Tool Weightage: 40%
Annexure A
SHORT ANSWER TEST
Code of Conduct:
I M.Monika / 192521435 (Name / Reg No) certify that this submission is my original work and that I have adhered to the guidelines specified for this assessment.
I understand that any violation of academic integrity rules will result in disciplinary action.
Signature of the student:
Monika . M

## Slide 2
Annexure A
Short Answer Test
A company needs to transfer a 150 MB design file from a client computer to a remote server over a network with a bandwidth of 50 Mbps. The Transport Layer divides the file into 1500-byte segments, while the Data Link Layer encapsulates each segment into frames by adding 40 bytes of header and trailer. Calculate the total number of segments and frames transmitted, the total transmission overhead introduced by the Data Link Layer, and estimate the total transmission time (ignoring propagation delay). Explain how the Transport and Data Link layers ensure reliable communication.
Solution:
File Transfer (150 MB)
File size = 150 MB = 150,000,000 bytes
Segment size = 1500 bytes
Number of segments = 150,000,000 ÷ 1500 = 100,000
Number of frames = 100,000
Overhead = 100,000 × 40 = 4,000,000 bytes (4 MB)
Total data transmitted = 154 MB
Transmission time = (154 × 8) ÷ 50 = 24.64 seconds
Explanation: The Transport Layer divides data into segments and provides error recovery. The Data Link Layer adds headers/trailers, frames the data, and detects transmission errors.
2. A Transport Layer protocol uses a sliding window size of 6 frames. Each frame carries 1024 bytes of user data. If the sender transmits 48 frames, calculate the number of transmission windows required. If one frame in every window is lost and must be retransmitted, determine the total number of retransmissions. Explain how flow control improves communication efficiency.
Solution:

## Slide 3
Sliding Window
Window size = 6
Total frames = 48
Number of windows = 48 ÷ 6 = 8
One frame lost per window = 8 retransmissions
Explanation: Flow control prevents the sender from sending data faster than the receiver can process, reducing congestion and improving efficiency.
3. A 12,000-byte IP packet is transmitted through a router where the Maximum Transmission Unit (MTU) is 1500 bytes. Assuming each fragment requires a 20-byte IP header, calculate the total number of fragments created and the total header overhead introduced. Explain how the Network Layer ensures successful delivery of fragmented packets to the destination.
Solution:
IP Fragmentation
IP packet = 12,000 bytes
MTU = 1500 bytes
Payload per fragment = 1500 − 20 = 1480 bytes
Fragments = ⌈12000 ÷ 1480⌉ = 9
Header overhead = 9 × 20 = 180 bytes
Explanation: The Network Layer fragments packets when needed and reassembles them at the destination for successful delivery.

## Slide 4
4. A Transport Layer protocol uses a sliding window size of 6 frames. Each frame carries 1024 bytes of user data. If the sender transmits 48 frames, calculate the number of transmission windows required. If one frame in every window is lost and must be retransmitted, determine the total number of retransmissions. Explain how flow control improves communication efficiency.
Solution:
Sliding Window
Transmission windows = 8
Retransmissions = 8
Explanation: Flow control balances the transmission speed between sender and receiver, improving communication reliability.
5. A multimedia application transfers a 600 MB video file. The Session Layer inserts a synchronization checkpoint after every 60 MB of transmitted data. During transmission, a failure occurs after 390 MB has been transferred. Determine the number of checkpoints created before failure and calculate the amount of data that must be retransmitted after recovery. Explain the importance of synchronization in the Session Layer.
Solution:
Session Layer
File size = 600 MB
Checkpoint every 60 MB
Failure after 390 MB
Checkpoints before failure = 6 (60,120,180,240,300,360)
Data to retransmit = 390 − 360 = 30 MB
Explanation: Synchronization checkpoints allow transmission to resume from the last checkpoint instead of restarting the entire transfer.

## Slide 5
6. Before transmission, the Presentation Layer compresses a 900 MB file by 40%. The compressed data is encrypted, adding 5% overhead to the compressed size. Calculate the compressed file size, the encrypted file size, and the total percentage reduction compared to the original file. Explain how the Presentation Layer improves transmission efficiency and security.
Solution:
Presentation Layer
Original size = 900 MB
Compression = 40%
Compressed size = 540 MB
Encryption overhead = 5% of 540 = 27 MB
Encrypted size = 567 MB
Reduction = ((900 − 567) ÷ 900) × 100 = 37%
Explanation: The Presentation Layer compresses data to reduce transmission size and encrypts it to ensure security.
7. An FTP application transfers 3 GB of data over a network with an effective throughput of 120 Mbps. The Application Layer divides the data into requests of 3 MB each. Calculate the total number of requests generated and estimate the total transmission time in seconds. Discuss how the Application Layer provides reliable services to users.
Solution:
FTP Transfer
Data = 3 GB = 3000 MB
Request size = 3 MB
Requests = 3000 ÷ 3 = 1000
Data in Mb = 24,000 Mb
Throughput = 120 Mbps
Transmission time = 24,000 ÷ 120 = 200 seconds
Explanation: The Application Layer provides user services such as FTP, manages file transfers, and ensures reliable communication.

## Slide 6
8. A packet experiences the following processing delays at different OSI layers: Application Layer = 4 ms, Transport Layer = 3 ms, Network Layer = 5 ms, Data Link Layer = 2 ms, and Physical Layer = 1 ms. The propagation delay is 18 ms, and the transmission delay is 12 ms. Calculate the total end-to-end delay experienced by the packet and explain how each layer contributes to the communication process.
Solutions:
End-to-End Delay
Processing delays:
Application = 4 ms
Transport = 3 ms
Network = 5 ms
Data Link = 2 ms
Physical = 1 ms
Total processing delay = 15 ms
Propagation delay = 18 ms
Transmission delay = 12 ms
Total end-to-end delay = 15 + 18 + 12 = 45 ms
Explanation: Each OSI layer performs a specific task, while transmission and propagation delays contribute to the total packet delay.
9. A network transfers 80 MB of useful data using frames of 1600 bytes, where each frame contains 80 bytes of protocol overhead added by different OSI layers. Calculate the total number of frames required, the total overhead transmitted, and the transmission efficiency as a percentage. Explain how protocol overhead affects network performance.
Solutions:
Frame Overhead
Useful data = 80 MB = 80,000,000 bytes
Frame size = 1600 bytes
Useful data per frame = 1600 − 80 = 1520 bytes
Frames = ⌈80,000,000 ÷ 1520⌉ = 52,632
Total overhead = 52,632 × 80 = 4,210,560 bytes
Efficiency = (1520 ÷ 1600) × 100 = 95%
Explanation: Protocol overhead reduces bandwidth available for actual data but is necessary for addressing, error detection, and reliable communication.

## Slide 7
10.A hospital transfers a patient's medical record of 240 MB through an IoT-enabled healthcare network. The Presentation Layer compresses the data by 30%, the Transport Layer divides the compressed data into 1400-byte segments, and the Data Link Layer adds 60 bytes of overhead to each frame. Calculate the compressed file size, the total number of segments transmitted, the total protocol overhead introduced, and the final amount of data transmitted across the Physical Layer. Explain how multiple OSI layers work together to ensure secure and reliable communication.
Solution:
Hospital IoT Network
Original file = 240 MB
Compression = 30%
Compressed size = 168 MB = 168,000,000 bytes
Segment size = 1400 bytes
Segments = 168,000,000 ÷ 1400 = 120,000
Overhead = 120,000 × 60 = 7,200,000 bytes (7.2 MB)
Final transmitted data = 168 + 7.2 = 175.2 MB
Explanation: The Presentation Layer compresses data, the Transport Layer segments it, the Data Link Layer adds frame overhead, and the Physical Layer transmits the data securely and reliably.

## Slide 8
RUBRICS FOR CALCULATION
Criteria | Weightag e | Level 4 – Exemplary | Level 3 – Proficient | Level 2 – Developing | Level 1 – Beginning
Understandin g of Concepts | 25% | Demonstrates a thorough, accurate understandin g of concepts | Good understanding with minor gaps | Basic understanding with some misconception s | Poor understanding; major misconception s
Explanation | 25% | Detailed, well-explained answers with relevant examples | Clear explanation with adequate details | Limited explanation; lacks depth | Poor or unclear explanation
Application | 20% | Effectively applies concepts with strong analytical ability | Applies concepts with minor errors | Limited application with weak analysis | No application or incorrect analysis
Organization | 15% | Well-structured answers with logical flow | Organized with minor issues in flow | Basic structure, lacks clarity | Poor organization, incoherent answers

## Slide 9
 |  | and coherence |  |  | 
Accuracy | 10% | Completely accurate and covers all required points | Mostly accurate with minor omissions | Partially correct with missing points | Incorrect answers with major gaps
Clarity | 5% | Clear, neat, professional presentation | Understandabl e with minor issues | Limited clarity, readability issues | Poorly written, difficult to understand