## Slide 1
Presented By:
Monika .M (192521435)
Satellite Internet Communication using OSI model
Technical presentation in Computer Networks
CSA0704 – Computer Networks

## Slide 2
Introduction to Satellite Internet & OSI Model
Satellite internet connects remote/ground terminals to the internet via satellites (GEO, MEO, LEO)
OSI model: 7-layer framework describing how data moves from application to physical transmission
Purpose: understand how each OSI layer functions specifically in a satellite communication context

## Slide 3
Layer 1 & 2 – Physical and Data Link Layer
Physical Layer: RF transmission over C, Ku, Ka, V-band; modulation (QPSK, 8PSK, 16APSK); Forward Error Correction (LDPC/BCH); propagation delay (~240-280 ms one-way for GEO)
Data Link Layer: Framing (DVB-S2/S2X); Multiple access methods (TDMA/FDMA/MF-TDMA); Error detection (CRC); ARQ for retransmission

## Slide 4
Layer 3 & 4 – Network and Transport Layer
Network Layer: IP routing between ground terminal, satellite, and gateway; addressing and path selection to reach the internet backbone
Transport Layer: TCP/UDP protocols; TCP performance tuning for high latency/loss (larger windows, Performance Enhancing Proxies - PEPs)

## Slide 5
Layer 5, 6 & 7 – Session, Presentation and Application Layer
Session Layer: Establishes, manages, and terminates communication sessions between devices
Presentation Layer: Data encryption (TLS/SSL), compression, format translation
Application Layer: End-user services — web browsing, email, video streaming, VoIP, DNS

## Slide 6
Challenges & Conclusion
Key challenges: high latency (~550-700 ms round trip for GEO), Doppler shift (LEO constellations), rain fade (especially Ka-band), signal attenuation over long distances
Conclusion: Every OSI layer is adapted to handle the unique challenges of satellite communication — distance, delay, and dynamic geometry

## Slide 7: THANKYOU!!